## Slide 1: SystemVerilog Lab 3 Single-Cycle Processor Part 2
Computer Architecture and Assembly Language – Fall 2024
By:
Eng. Alaa Mohamed – Eng. Mohamed Ali

## Slide 2: Single-Cycle Processor

## Slide 3: Single-Cycle Processor HDL
Top

## Slide 4: Single-Cycle Processor Integration
Top

## Slide 5: Datapath

## Slide 6: Single Cycle Processor Datapath
6
Top

## Slide 7: Building Modules
These parameterized modules are either previously done or given:
  2-to-1 Multiplexer
  Resettable Flip-flop
  Adder
  ALU (ADD, SUB, AND, ORR)
This lab task include implementing the following modules:
  Extender
  Register File
It is also required to integrate the modules to make the datapath module.

## Slide 8: Extender

## Slide 9: Extender: Immediate Src2
1
2
3

## Slide 10: Extender: Immediate Src2
1
2
3

## Slide 11: Register File

## Slide 12: Register File Specs
Contains fifteen 32-bit register (2D array).
Read operation is done combinationally, while write operation is done at the rising edge of the clock.
Input ports:
  clk
  A1: read address 1
  A2: read address 2
  A3: write address
  WD3: write data
  WE3: write enable
  R15: special for reading PC+8

## Slide 13: Register File Specs
Contains fifteen 32-bit register (2D array).
Read operation is done combinationally, while write operation is done at the rising edge of the clock.
Output ports:
  RD1: read data 1
  RD2: read data 2

## Slide 14: Recap: Sub-Modules Instantiation
A design can use multiple submodules or a module multiple times.
Using a module in another is called “instantiation”.
To use a module inside another, it should be explicitly instantiated.

## Slide 15: Recap: Sub-Modules Instantiation
To instantiate a module, two things have to be clearly specified:
  Module’s ports
  Module’s parameters (considered as default if not specified)
Named Assignment format:
  Module_name #(parameter_value) instance_name (.port_name(port-connection), .port_name(port-connection),….)
Ordered Assignment format:
  Module_name #(parameter_value) instance_name (port-connection, port-connection,….)
  Example: flopenr #(2) flagreg0 (clk, reset, FlagWrite[0], ALUFlags[1:0], Flags[1:0]);

## Slide 16: Controller

## Slide 17: Single-Cycle Processor Controller
Top

## Slide 18: Control Unit

## Slide 19: Control Unit

## Slide 20: Building Modules
These modules are given:
  Resettable Flip-flop with Enable
  Conditional Logic
  ALU Decoder
  PC Logic
  Controller (top-level module)
This lab task include implementing the following modules:
  Conditional Check
  Main Decoder (inside decoder module)

## Slide 21: Conditional Check
Inputs:
  Cond (4 bits)
  Flags (4 bits)  (N, Z, C, V)
Output:
  CondEx (1 bit)
The module checks whether to update (write) the destination register based on the condition mnemonic and saved flags.

## Slide 22: Conditional Check
Inputs:
  Cond (4 bits)
  Flags (4 bits)  (N, Z, C, V)
Output:
  CondEx (1 bit)
The module checks whether to update (write) the destination register based on the condition mnemonic and saved flags.

## Slide 23: Main Decoder
Inputs
Outputs

## Slide 24: Instruction and Data Memories

## Slide 25: Single-Cycle Processor Integration
Top

## Slide 26: Instruction Memory (64 * 32 bits)
The test program instructions’ machine code is stored in a hexadecimal file called memfile.dat.
The instruction memory module reads this file and outputs the instruction based on the value of PC (input).
PC increases by 4 in hardware, while array index
should increase by 1 in SystemVerilog module.
Word alignment acts as a two-bit right shifter
(dividing by 4) as follows:
  assign rd = RAM[a[31:2]];

## Slide 27: Data Memory (64 * 32 bits)
Read operation is done combinationally, while write operation is done at the rising edge of the clock.
Word alignment should be applied on input address.
Inputs:
  Clk
  WE (1 bit)  write enable
  A (32 bits)  read or write address
  WD (32 bits)  write data
Output:
  RD (32 bits)  read data

## Slide 28: Top Level Module

## Slide 29: Testbench
The program, stored in instruction memory, exercises hardware by performing a computation that should produce the correct result only if all of the instructions are functioning correctly.
Specifically, the program will write the value 7 to address 100 if it runs correctly, but it is unlikely to do so if the hardware is buggy.

## Slide 30: Testbench
Top
TB
Drive inputs
Observe outputs